Kane's Method Applied to the Dynamics of Spacecraft Composed of Multiple Flexible Bodies
Eric Stoneking
October 2010

---
“F = ma. The rest is just accounting.”

---
Modelling A Flexible Body

---
Deflection of a Mass Element
Deformed
d
Reference Origin
%delta
r
Undeformed

---
Velocity and Acceleration of a Mass Element
Define translational and angular deformation velocities:
matrix{e_k # "=" # dot{d_k} ## %epsilon_k # "=" # dot{%delta_k}}
Then we can express the total (including rigid and flexible motion) velocity
and acceleration of the mass element as:
alignl{stack{ {breve{v}}_k = v + %omega times (r_k+d_k) + e_k # {breve{a}}_k = a + %omega times left [ %omega times (r_k + d_k) right ] + %alpha times (r_k + d_k) + {dot{e}}_k + 2 %omega times e_k}}
"where the undecorated" `%omega,`v,`%alpha,` "and" `a` "describe the motion of the body's" newline "reference point"

---
This Could Get Out of Hand...
- To formulate dynamic EOM, we need the acceleration of every mass element in the system
  - For a particle, there are only 3 DOF. Easy.
  - For a rigid body, there are only 6 DOF. Not bad.
- For a flexible body, how do we avoid infinite DOF?
  - Assumed modes, truncated to N most interesting
F=ma
F=ma,~~T = I%alpha - %omega times H

---
Assumed Modes (1)
Consider flexible deformation to be a linear combination of a finite number of independent modes. For mass element k,
Translational
Mode Shapes
Translational
deflection
left lbrace stack{d_k # %delta_k} right rbrace = left [ stack{%PSI_k # %THETA_k} right ] left lbrace %eta right rbrace
%xi equiv dot{%eta}
and
Modal
Coordinates
Rotational
Mode Shapes
Angular
deflection
Q: Where do mode shapes come from?
A1: Solid mechanics of beam, rod, column, etc, OR
A2: NASTRAN or other Finite Element Modelling
        software, OR
A3: Specify by axis, frequency, damping, modal mass

---
Assumed Modes (2)
The units of are somewhat arbitrary,
as long as have units of length, angle.
One common choice is “mass-normalized”:
%eta, %PSI, %THETA
d, %delta
[%eta] = m sqrt{kg}, ~~ [%PSI] = 1 over sqrt{kg}, ~~ [%THETA] = rad over {m sqrt{kg}}
Another obvious choice is simply dimensionless
modal coordinates:
[%eta] = 1,~~ [%PSI] = m,~~ [%THETA] = rad

---
Assumed Modes (3)
- Assuming N modes, are each of dimension 3xN for each mass element.
- In practice, we are only interested in the motions of a few points, not every mass element
  - Joint motions are needed for multibody kinematics
  - Motion of sensor locations may be needed for proper measurement modeling
  - Points of application of forces (e.g. thrusters) may be needed to properly capture modal excitation
- But we do need to account for the effects of flexibility integrated over the entire body
%PSI_k, %THETA_k

---
Free-Free vs. Cantilever
Mode Shapes
- Free-Free mode shapes assume body is unconstrained
  - Flexible motion does not move mass center
  - Use mass center as reference point for acceleration formulation
    - Some modal integrals integrate to zero!
  - Multibody kinematics must account for deflections of joints
- Cantilever mode shapes fix body at some point which is not the mass center
  - Use that point as reference point for acceleration formulation
  - If that point is a joint, some terms drop out of the multibody kinematics
    - Non-contributing constraint forces at the joints are eliminated from the equations of motion (but Kane's method eliminates non-contributing forces anyway)
  - Modal integrals are non-zero (as are first mass moments of rigid body)

---
Equations of Motion for
One Flexible Body

---
Formulating Equations of Motion (1)
For a rigid body, Kane's equations may be written
%OMEGA^T lbrace T-I%alpha-%omega times H rbrace + V^T lbrace F - m a rbrace = 0
For a flexible body, we combine Newton's law with the moment about our reference point,
and integrate over the body:
int lbrace %OMEGA^T left[ d%tau-(r+d) times breve{a}dm right] + V^T left[ df - breve{a}dm right] rbrace = 0
alignl "Using the generalized speeds"~left lbrace stack{u # %xi} right rbrace, "we may write:" newline breve{%omega} = %omega = left [ %OMEGA_u ~~%OMEGA_%xi right ] left lbrace stack{u # %xi} right rbrace, ~~breve{v} = v + %PSI %xi = left [ %V_u ~~%V_%xi + %PSI right ] left lbrace stack{u # %xi} right rbrace newline alignl "where" ~%OMEGA_u, `%OMEGA_%xi, `%V_u,` "and" `%V_%xi `"account for motion of the reference point." newline alignl "These partial velocities are constant over a body." newline newline alignl "For a single body, "~%OMEGA_u, `%OMEGA_%xi, `%V_u,` "and" `%V_%xi `"are trivial (" U,` 0,` U,` 0, " respectively), "newline "so it's tempting to drop them from the formalism. They will play a key role, " newline "however, when we assemble multi-body systems.

---
Formulating Equations of Motion (2)
The acceleration terms may be integrated over the body:
matrix{int breve{a}dm # "=" # alignl int {left[ a + %omega times %omega times (r+%PSI %eta) + %alpha times (r+%PSI %eta) + %PSI dot{%xi} + 2 %omega times %PSI %xi right]}dm ## " " # "=" # alignl ma + %omega times %omega times (c + P_%psi %eta) + %alpha times (c + P_%psi %eta) + P_%psi dot{%xi} + 2 %omega times P_%psi %xi}
matrix{int (r+d) times breve{a} dm # "=" #alignl int (r+%PSI %eta) times left[ a + %omega times %omega times (r+%PSI %eta) + %alpha times (r+%PSI %eta) + %PSI dot{%xi} + 2 %omega times %PSI %xi right] dm ## " " # "=" # alignl c times a + P_%psi %eta times a + J %alpha + %omega times J %omega + (H_%psi + Q_%PSI %eta) dot{%xi}
"(Most terms that are second-order in "` %eta, %xi " have been dropped.)"
Some useful “modal integrals” appear:
c = int rdm, ~~ P_%psi = int %PSI dm, ~~J =-int r^{" " times " "} r^{" " times " "} dm, ~~H_%psi = int r^{" " times " "} %PSI dm
"(If our reference point is the center of mass, then"~ J toward I, `"and"~c = P_%psi = H_%psi = 0 ")"
Q_%PSI " is a 3xNxN tensor that will be defined on slide 17."

---
Formulating Equations of Motion (3)
So the equations of motion are (so far):
left [ stack{%OMEGA^T_u # %OMEGA^T_%xi} right ] left lbrace {T - left [ J %alpha + %omega times J %omega + (c + P_%psi %eta) times a + (H_%psi+Q_%PSI %eta) dot{%xi} right ]} right rbrace "+" newline left [ stack{V^T_u # V^T_%xi} right ] left lbrace {F - left [ ma + %alpha times (c + P_%psi %eta) + %omega times (%omega times (c + P_%psi %eta)) + P_%psi dot{%xi} + 2 %omega times P_%psi %xi right ]} right rbrace "+" newline left lbrace stack{0 # int %PSI^T left [ df - breve{a}dm right ]} right rbrace = 0

---
More Modal Integrals (1)
We've already introduced these modal integrals:
c = int rdm, ~~ P_%psi = int %PSI dm, ~~J =-int r^{" " times " "} r^{" " times " "} dm, ~~H_%psi = int r^{" " times " "} %PSI dm
In the derivation to follow, we will also need:
M_%PSI = int { %PSI^T %PSI} dm, ~~ {L_ijp} underbrace {3 times 3 times N} = int {%PSI_ip r_j} dm, ~~ {N_ijpq} underbrace {3 times 3 times N times N} = int {%PSI_ip %PSI_jq} dm
L_ijp " and " N_ijpq " capture all possible products of "~%PSI " with " r " or with itself. We could, in fact," newline "construct "~ H_%PSI " and " M_%PSI " from elements of " L_ijp " and " N_ijpq ", respectively."newline newline "Some other tensors derived from " L_ijp " and "N_ijpq" will also be needed. We define them" newline "in the following slides, and label them "Q_%PSI, R_%PSI, "and "S_%PSI .

---
More Modal Integrals (2)
"It will be convenient to denote the rows of "~%PSI " as" ~%PSI = left lbrace {stack { %PSI_1 # %PSI_2 # %PSI_3 } } right rbrace " and partially expand "L_ijp" and "N_ijpq":"
L_ijp = left [ matrix {L_11 # L_12 # L_13 ## L_21 # L_22 # L_23 ## L_31 # L_32 # L_33} right ] = int{left [ matrix {%PSI_1 r_1 # %PSI_1 r_2 # %PSI_1 r_3 ## %PSI_2 r_1 # %PSI_2 r_2 # %PSI_2 r_3 ## %PSI_3 r_1 # %PSI_3 r_2 # %PSI_3 r_3 } right ]} dm newline newline newline N_ijpq = left [ matrix {N_11 # N_12 # N_13 ## N_21 # N_22 # N_23 ## N_31 # N_32 # N_33} right ] = int {left [ matrix {%PSI_1^T %PSI_1 # %PSI_1^T %PSI_2 # %PSI_1^T %PSI_3 ## %PSI_2^T %PSI_1 # %PSI_2^T %PSI_2 # %PSI_2^T %PSI_3 ## %PSI_3^T %PSI_1 # %PSI_3^T %PSI_2 # %PSI_3^T %PSI_3 } right ]} dm
L_ij " is an N-element vector, and " N_ij " is an N-by-N matrix."

---
More Modal Integrals (3)
"We can then introduce:" newline newline alignl Q_%PSI equiv left [ matrix{ N_32-N_23 ## N_13-N_31 ## N_21-N_12} right ]~~~(3 times N times N) newline newline alignl R_%PSI equiv left [ alignc matrix{ -L_22-L_33 # L_21 # L_31 ## L_12 # -L_33-L_11 # L_32 ## L_13 # L_23 # -L_11-L_22} right ] ~~~(3 times N times 3) newline newline alignl S_%PSI equiv left [ alignc matrix{-N_22-N_33 # N_21 # N_31 ## N_12 # -N_33-N_11 # N_32 ## N_13 # N_23 # -N_11-N_22} right ] ~~~(3 times N times N times 3)

---
Expansion of
int %PSI^T df
alignl df " refers to any forces, internal or external, acting on the flexible body. For" newline "example, suppose the body material obeys Hooke's Law:" newline df_K = -Sd = -S %PSI %eta dV newline "where " S " is the (3 x 3) material elasticity matrix relating stress and strain. (See Appendix)" newline "Substituting, we find the familiar modal stiffness force term:" newline f_K = int {%PSI^T df_K} = int_V {(-%PSI^T S %PSI %eta)} dV newline f_K = -K_%PSI %eta newline "where " K_%PSI " is the familiar modal stiffness matrix." newline "Similar arguments may be used for a Coulomb damping term, " f_C = -C_%PSI %xi, " and any other" newline "internal forces required." newline newline "The effect of external forces and torques on flexible modes is denoted by:" newline breve{F} = int %PSI^T df_{ext} newline breve{T} = int %THETA^T d%tau_{ext} newline "See following slides for an illustrative example."

---
Flexible Mode Excitation by External Forces and Torques
- In the development so far, F and T denote the resultant force and torque exerted on the body by external forces and torques, applied to the reference point.
- To capture the excitation of flexible modes by external forces and torques, their points of application must be projected into the modal state space.

---
Modal Excitation Example 1
- Consider a flexible body with free-free mode shapes and reference point at the mass center
- The force system shown has zero resultant force and torque, but excites a bending mode
- Moral: Modeling of applied forces and torques must account for distribution over the body to capture influence on flexible modes.
alignl F = int df = 0 newline alignl T = int r times df = 0 newline alignl breve{F} = int %PSI^T df <> 0
f
f
2f
r
r

---
Modal Excitation Example 2
- Consider a flexible body with free-free mode shapes and reference point at the mass center
- The force system shown has zero resultant force and torque, but excites a bending mode
- Moral: Modeling of applied forces and torques must account for distribution over the body to capture influence on flexible modes.
%tau
alignl F = int df = 0 newline alignl T = int r times df = 0 newline alignl breve{T} = int %THETA^T d%tau <> 0
%tau

---
Expansion of
- int %PSI^T breve{a}dm
- int { %PSI^T breve{a}} dm = - int { %PSI^T left lbrace a + %omega times left [ %omega times (r + %PSI %eta) right ] + %alpha times (r + %PSI %eta) + %PSI dot{%xi} + 2 %omega times %PSI %xi right rbrace } dm
"Expand each term, taking constants out of the integral. Terms 1, 4, and 6 are" newline "short work. The remaining terms will be expanded in following slides." newline newline "Term 1: "~ -int %PSI^T a dm = -(int %PSI^T dm) a = -P^T_%PSI a newline "Term 2: "~ -int %PSI^T left [ %omega times ( %omega times r ) right ] dm newline "Term 3: "~ -int %PSI^T left [ %omega times ( %omega times %PSI %eta ) right ] dm newline "Term 4: "~ -int %PSI^T ( %alpha times r ) dm = -int (r times %PSI) cdot %alpha dm = -H^T_%PSI %alpha newline "Term 5: "~ -int %PSI^T ( %alpha times %PSI %eta ) dm newline "Term 6: "~ -int %PSI^T %PSI dot{%xi} dm = -(int %PSI^T %PSI dm) dot{%xi} = -M_%PSI dot{%xi} newline "Term 7: "~ -2 int %PSI^T (%omega times %PSI %xi) dm

---
Expansion of Term 2
"Term 2: "~ - int %PSI^T left [ %omega times ( %omega times r ) right ] dm newline "Expand to "~ -int left [ matrix { %PSI^T_1 # %PSI^T_2 # %PSI^T_3 } right ] left lbrace matrix { %omega_2 ( %omega_1 r_2 - %omega_2 r_1) - %omega_3 (%omega_3 r_1 - %omega_1 r_3) ## %omega_3 ( %omega_2 r_3 - %omega_3 r_2) - %omega_1 (%omega_1 r_2 - %omega_2 r_1) ## %omega_1 ( %omega_3 r_1 - %omega_1 r_3) - %omega_2 (%omega_2 r_3 - %omega_3 r_2) } right rbrace dm newline "then "~~~~~~~~~ -int %PSI^T_1 left [ r_1 (-%omega^2_2-%omega^2_3) + r_2 %omega_1 %omega_2 + r_3 %omega_1 %omega_3 right ] newline + %PSI^T_2 left [ r_1 %omega_2 %omega_1 + r_2 (-%omega^2_3-%omega^2_1) + r_3 %omega_2 %omega_3 right ] newline ~~~+ %PSI^T_3 left [ r_1 %omega_3 %omega_1 + r_2 %omega_3 %omega_2 + r_3 (-%omega^2_1-%omega^2_2) right ] dm newline newline "and finally:
alignl - int %PSI^T left [ %omega times ( %omega times r ) right ] dm = L_11 (%omega^2_2 +%omega^2_3) + L_22 (%omega^2_3 +%omega^2_1) + L_33 (%omega^2_1 +%omega^2_2) newline ~~~~~~~~~~~~~~~~~~~~~~~~~~ - (L_12+L_21) %omega_1 %omega_2 - (L_13+L_31) %omega_1 %omega_3 - (L_23+L_32) %omega_2 %omega_3
"For brevity in the ensuing development, we use "R_%PSI", so" newline -int %PSI^T left [ %omega times ( %omega times r ) right ] dm = -%omega cdot R_%PSI cdot %omega

---
Expansion of Term 3
"Term 3: "~ - int %PSI^T left [ %omega times ( %omega times %PSI %eta ) right ] dm newline newline "Follow the example of term 2, replacing"~r~"with"~%PSI %eta: newline ~ -int left [ matrix { %PSI^T_1 # %PSI^T_2 # %PSI^T_3 } right ] left lbrace matrix { %omega_2 (%omega_1 %PSI_2 %eta - %omega_2 %PSI_1 %eta) - %omega_3 (%omega_3 %PSI_1 %eta - %omega_1 %PSI_3 %eta) ## %omega_3 (%omega_2 %PSI_3 %eta - %omega_3 %PSI_2 %eta) - %omega_1 (%omega_1 %PSI_2 %eta - %omega_2 %PSI_1 %eta) ## %omega_1 (%omega_3 %PSI_1 %eta - %omega_1 %PSI_3 %eta) - %omega_2 (%omega_2 %PSI_3 %eta - %omega_3 %PSI_2 %eta) } right rbrace dm newline "then "~~~~~~~~~ -int %PSI^T_1 left [ %PSI_1 (-%omega^2_2-%omega^2_3) + %PSI_2 %omega_1 %omega_2 + %PSI_3 %omega_1 %omega_3 right ] %eta newline + %PSI^T_2 left [ %PSI_1 %omega_2 %omega_1 + %PSI_2 (-%omega^2_3-%omega^2_1) + %PSI_3 %omega_2 %omega_3 right ] %eta newline ~~~+ %PSI^T_3 left [ %PSI_1 %omega_3 %omega_1 + %PSI_2 %omega_3 %omega_2 + %PSI_3 (-%omega^2_1-%omega^2_2) right ] %eta dm newline newline "and finally:
alignl - int %PSI^T left [ %omega times ( %omega times %PSI %eta ) right ] dm = "[" N_11 (%omega^2_2 +%omega^2_3) + N_22 (%omega^2_3 +%omega^2_1) + N_33 (%omega^2_1 +%omega^2_2) newline ~~~~~~~~~~~~~~~~~~~~~~~~~~~~ - (N_12+N_21) %omega_1 %omega_2 - (N_13+N_31) %omega_1 %omega_3 - (N_23+N_32) %omega_2 %omega_3 "]" %eta
"For brevity in the ensuing development, we use "S_%PSI" so" newline -int %PSI^T left [ %omega times ( %omega times %PSI %eta ) right ] dm = -%omega cdot S_%PSI cdot %omega %eta

---
Expansion of Term 5
alignl "Term 5: "-int %PSI^T ( %alpha times %PSI %eta ) dm newline newline "Expand as:"~~-int left [ matrix{%PSI^T_1 # %PSI^T_2 # %PSI^T_3} right ] left lbrace matrix { %alpha_2 %PSI_3 %eta - %alpha_3 %PSI_2 %eta ## %alpha_3 %PSI_1 %eta - %alpha_1 %PSI_3 %eta ## %alpha_1 %PSI_2 %eta - %alpha_2 %PSI_1 %eta } right rbrace dm newline "which reduces to:" newline newline -int %PSI^T ( %alpha times %PSI %eta ) dm = - %eta^T left [ matrix{(N_32-N_23)# (N_13-N_31)# (N_21-N_12)} right ] %alpha
"For brevity in the ensuing development, we use "~ Q_%PSI, " so" newline -int %PSI^T ( %alpha times %PSI %eta ) dm = - %eta^T Q_%PSI^T %alpha

---
Expansion of Term 7
alignl "Term 7: "-2 int %PSI^T ( %omega times %PSI %xi ) dm newline newline "As with term 5, expand as:"~~-2 int left [ matrix{%PSI^T_1 # %PSI^T_2 # %PSI^T_3} right ] left lbrace matrix { %omega_2 %PSI_3 %xi - %omega_3 %PSI_2 %xi ## %omega_3 %PSI_1 %xi - %omega_1 %PSI_3 %xi ## %omega_1 %PSI_2 %xi - %omega_2 %PSI_1 %xi } right rbrace dm newline "which reduces to:" newline newline newline -2 int %PSI^T ( %omega times %PSI %xi ) dm = -2 %xi^T left [ matrix{(N_32-N_23) # (N_13-N_31) # (N_21-N_12)} right ] %omega
"For brevity in the ensuing development, we use "~ Q_%PSI, " so" newline -2 int %PSI^T ( %omega times %PSI %xi ) dm = -2 %xi^T Q_%PSI^T %omega

---
Equations of Motion for
One Flexible Body
"Reassembling, and including forces due to material stiffness and damping " newline "as examples of internal forces, we obtain" newline newline breve{F} + breve{T} - M_%PSI dot{%xi} - C_%PSI %xi - K_%PSI %eta - P^T_%PSI a - (H^T_%PSI+%eta^T Q_%PSI^T) %alpha - %omega cdot R_%PSI cdot %omega - %omega cdot S_%PSI cdot %omega %eta -2 %xi^T Q_%PSI^T %omega = 0
Inserting into the overall equations of motion from slide 15:
left [ stack{%OMEGA^T_u # %OMEGA^T_%xi} right ] left lbrace {T - left [ J %alpha + %omega times J %omega + (c + P_%psi %eta) times a + (H_%psi+Q_%PSI %eta) dot{%xi} right ]} right rbrace "+" newline left [ stack{V^T_u # V^T_%xi} right ] left lbrace {F - left [ ma + %alpha times (c + P_%psi %eta) + %omega times (%omega times (c + P_%psi %eta)) + P_%psi dot{%xi} + 2 %omega times P_%psi %xi right ]} right rbrace "+" newline left lbrace stack{0 # breve{F} + breve{T} - M_%PSI dot{%xi} - C_%PSI %xi - K_%PSI %eta - P^T_%PSI a - (H^T_%PSI+%eta^T Q_%PSI^T) %alpha - %omega cdot R_%PSI cdot %omega - %omega cdot S_%PSI cdot %omega %eta -2 %xi^T Q_%PSI^T %omega} right rbrace = 0

---
Simplified EOM for
One Free-Free Body
"For a single body, the equations of motion may be written:" newline newline left [ matrix{ J # (c+P_%PSI %eta)^{`times`} # (H_%PSI+Q_%PSI %eta) ## -(c+P_%PSI %eta)^{`times`} # m U # P_%PSI ## (H_%PSI+Q_%PSI %eta)^T # P_%PSI^T # M_%PSI } right ] left lbrace matrix{ dot %omega ## dot v ## dot %xi } right rbrace = left lbrace matrix{ T-%omega times J %omega ## F - %omega times left [ %omega times(c+P_%PSI %eta) right ] -2 %omega times P_%PSI %xi ## breve{F} + breve{T} - C_%PSI %xi - K_%PSI %eta- %omega cdot R_%PSI cdot %omega - %omega cdot S_%PSI cdot %omega %eta -2 %xi^T Q_%PSI^T %omega } right rbrace newline newline "Using the mass center as the reference point, and dropping nonlinear " newline "rigid-flexible coupling terms:" newline newline left [ matrix{ I # 0 # 0 ## 0 # m U # 0 ## 0 # 0 # M_%PSI } right ] left lbrace matrix{ dot %omega ## dot v ## dot %xi } right rbrace = left lbrace matrix{ T-%omega times I %omega ## F ## breve{F} + breve{T} - C_%PSI %xi - K_%PSI %eta } right rbrace newline newline "which is reassuringly familiar. Note that the flexible modes are only coupled to rigid-body " newline "motion through excitation by " breve{F} " and " breve{T}"!"

---
Observations
If modes are mass-normalized, then
- is sometimes assumed to be diagonal
  - But the full stress-strain relation leads to off-diagonal stiffness elements
  - These off-diagonal elements become important for “fast” motions
  - Neglecting them yields poor (even nonphysical) results
M_%PSI = U, ~~~ K_%PSI = left [ matrix{dotsdown #~#~##~#%omega^2_%PSI#~##~#~#dotsdown} right ]
K_%PSI

---
Equations of Motion for
Multiple Flexible Bodies
in a Tree Topology

---
The Rest Is Just Accounting
"Substitute " %alpha = %OMEGA_u dot{u} + %OMEGA_%xi dot{%xi} + %alpha_r,~a = %V_u dot{u} + V_%xi dot{%xi} + a_r " into equations of motion,"
left [ stack{%OMEGA^T_u # %OMEGA^T_%xi} right ] left lbrace {T - left [ J %alpha + %omega times J %omega + (c + P_%psi %eta) times a + (H_%psi+Q_%PSI %eta) dot{%xi} right ]} right rbrace "+" newline left [ stack{V^T_u # V^T_%xi} right ] left lbrace {F - left [ ma + %alpha times (c + P_%psi %eta) + %omega times (%omega times (c + P_%psi %eta)) + P_%psi dot{%xi} + 2 %omega times P_%psi %xi right ]} right rbrace "+" newline left lbrace stack{0 # breve{F} + breve{T} - M_%PSI dot{%xi} - C_%PSI %xi - K_%PSI %eta - P^T_%PSI a - (H^T_%PSI+%eta^T Q_%PSI^T) %alpha - %omega cdot R_%PSI cdot %omega - %omega cdot S_%PSI cdot %omega %eta -2 %xi^T Q_%PSI^T %omega} right rbrace = 0
"and group terms on "dot{u}, dot{%xi}:

---
Equations of Motion
"Let" newline alignl Z_1 = J %OMEGA_u + (c+P_%PSI %eta) times V_u newline alignl Z_2 = m V_u - (c+P_%PSI %eta) times %OMEGA_u newline alignl Z_3 = J %OMEGA_%xi + (c+P_%PSI %eta) times V_%xi + (H_%PSI + Q_%PSI %eta) newline alignl Z_4 = m V_%xi - (c+P_%PSI %eta) times %OMEGA_%xi + P_%PSI newline alignl Z_5 = T-J %alpha_r - %omega times J %omega - (c+P_%PSI %eta) times a_r newline alignl Z_6 = F - m a_r - %alpha_r times (c+P_%PSI %eta) - %omega times left [ %omega times (c+P_%PSI %eta) right ] - 2 %omega times P_%PSI %eta
"Then " newline newline left [ matrix{%OMEGA_u^T Z_1 + V_u^T Z_2 # %OMEGA_u^T Z_3 + V_u^T Z_4 ## %OMEGA_%xi^T Z_1 + V_%xi^T Z_2 +P_%PSI^T V_u + (H_%PSI^T + %eta^T Q_%PSI^T) %OMEGA_u # %OMEGA_%xi^T Z_3 + V_%xi^T Z_4 + M_%PSI + P_%PSI^T V_%xi + (H_%PSI^T+%eta^T Q_%PSI^T)%OMEGA_%xi} right ] left lbrace matrix{dot{u} ## dot{%xi}} right rbrace = ~ newline newline left lbrace matrix{%OMEGA_u^T Z_5 + V_u^T Z_6 ## %OMEGA_%xi^T Z_5 + V_%xi^T Z_6 + breve{F}+breve{T}-C_%PSI %xi - K_%PSI %eta -P_%PSI^T a_r - (H_%PSI^T + %eta^T Q_%PSI^T) %alpha_r - %omega cdot R_%PSI cdot %omega - %omega cdot S_%PSI cdot %omega %eta - 2 %xi^T Q_%PSI^T %omega} right rbrace

---
Equations of Motion (with Bases)
"Let" newline alignl Z_1 = J %OMEGA_u + (c+P_%PSI %eta) times C lsup B rsup N V_u newline alignl Z_2 = m V_u - C lsup N rsup B(c+P_%PSI %eta) times %OMEGA_u newline alignl Z_3 = J %OMEGA_%xi + (c+P_%PSI %eta) times C lsup B rsup N V_%xi + (H_%PSI + Q_%PSI %eta) newline alignl Z_4 = m V_%xi - C lsup N rsup B left [ (c+P_%PSI %eta) times %OMEGA_%xi - P_%PSI right ] newline alignl Z_5 = T-J %alpha_r - %omega times J %omega - (c+P_%PSI %eta) times C lsup B rsup N a_r newline alignl Z_6 = F - m a_r - C lsup N rsup B left lbrace %alpha_r times (c+P_%PSI %eta) + %omega times left [ %omega times (c+P_%PSI %eta) right ] + 2 %omega times P_%PSI %eta right rbrace
"Then " newline newline left [ matrix{%OMEGA_u^T Z_1 + V_u^T Z_2 # %OMEGA_u^T Z_3 + V_u^T Z_4 ## %OMEGA_%xi^T Z_1 + V_%xi^T Z_2 +P_%PSI^T C lsup B rsup N V_u + (H_%PSI^T + %eta^T Q_%PSI^T) %OMEGA_u # %OMEGA_%xi^T Z_3 + V_%xi^T Z_4 + M_%PSI + P_%PSI^T C lsup B rsup N V_%xi + (H_%PSI^T+%eta^T Q_%PSI^T)%OMEGA_%xi} right ] left lbrace matrix{dot{u} ## dot{%xi}} right rbrace = ~ newline newline left lbrace matrix{%OMEGA_u^T Z_5 + V_u^T Z_6 ## %OMEGA_%xi^T Z_5 + V_%xi^T Z_6 + breve{F}+breve{T}-C_%PSI %xi - K_%PSI %eta -P_%PSI^T C lsup B rsup N a_r - (H_%PSI^T + %eta^T Q_%PSI^T) %alpha_r - %omega cdot R_%PSI cdot %omega - %omega cdot S_%PSI cdot %omega %eta - 2 %xi^T Q_%PSI^T %omega} right rbrace

---
Remainder Accelerations
"We have expressed linear and angular accelerations as:" newline a = %V_u dot{u} + %V_%xi dot{%xi} + a_r newline %alpha = %OMEGA_u dot{u} + %OMEGA_%xi dot{%xi} + %alpha_r newline "where " a_r " and " %alpha_r " simply denote whatever terms in "` a " and "%alpha" do not depend on "` dot{u} " and " dot{%xi}. newline "For lack of a better term, we call these the remainder accelerations." newline newline "Consider an inner body, "`B_i", and an outer body, "`B_o", connected by joint "`G_k"." newline "We may write the recursive expressions:" newline newline %alpha_ro = %alpha_ri + {dot{%GAMMA}}_k %sigma_k + %omega_o times %GAMMA_k %sigma_k + %omega_i times %THETA_ik %xi_i - %omega_o times %THETA_ok %xi_o newline a_ro = a_ri + %omega_i times (%omega_i times {breve{r}}_ik) - %omega_o times (%omega_o times {breve{r}}_ok) + %alpha_ri times {breve{r}}_ik - %alpha_ro times {breve{r}}_ok + 2(%omega_i times %PSI_ik %xi_i - %omega_o times %PSI_ok %xi_o)

---
Partial Velocities
"Partial velocities, " V = [V_u~ V_%xi] " and partial angular velocities" %OMEGA = [%OMEGA_u~ %OMEGA_%xi]" reflect the " newline "kinematics of the multibody spacecraft as a whole. It is easiest to define them by " newline "way of example." newline newline "Consider the five-body spacecraft illustrated on the next slide. We will write " newline "linear and angular velocities for all bodies, and look for helpful patterns to emerge."
"As with the remainder accelerations, we can form recursive expressions for the angular" newline "and linear velocity of an outer body "(B_o)" in terms of its inner body "(B_i)" and the joint "(G_k) newline " they share:"newline %omega_o = %omega_i + %GAMMA_k %sigma_k + %THETA_ik %xi_i - %THETA_ok %xi_o newline %v_o = v_i + %omega_i times {breve{r}}_ik - %omega_o times {breve{r}}_ok + %PSI_ik %xi_i - %PSI_ok %xi_o

---
Example Problem
"Define " %beta_i " to be the vector from the " newline "origin of " B_i " to the origin of " B_1 . newline newline "Define " %rho_ik " to be the vector from the " newline "origin of " B_i " to the joint " G_k .
B_1 B_2 B_3 B_4 B_5 G_1 G_2 G_3 G_4 vec p_1 {vec r}_11 {vec r}_21 {vec r}_12 {vec r}_32 {vec r}_33 {vec r}_34 {vec r}_43 {vec r}_54
N

---
Example Partial Velocities
left lbrace {matrix{%omega_1 ## %omega_2 ## %omega_3 ## %omega_4 ## %omega_5 }} right rbrace = {left [ {matrix{U # 0 # 0 # 0 # 0 # 0 ## C lsup 2 rsup 1 # %GAMMA_1 # 0 # 0 # 0 # 0 ## C lsup 3 rsup 1 # 0 # %GAMMA_2 # 0 # 0 # 0 ## C lsup 4 rsup 1 # 0 # C lsup 4 rsup 3 %GAMMA_2 # %GAMMA_3 # 0 # 0 ## C lsup 5 rsup 1 # 0 # C lsup 5 rsup 3 %GAMMA_2 # 0 # %GAMMA_4 # 0}}right ]} underbrace {%OMEGA_u} {left lbrace {matrix{%omega_1 ## %sigma_1 ## %sigma_2 ## %sigma_3 ## %sigma_4 ## v_1}} right rbrace} underbrace {u}+ left [ matrix{0 # 0 # 0 # 0 # 0 ## C lsup 2 rsup 1 %THETA_11 # -%THETA_21 # 0 # 0 # 0 ##C lsup 3 rsup 1 %THETA_12 # 0 # -%THETA_32 # 0 # 0 ## C lsup 4 rsup 1 %THETA_12 # 0 # C lsup 4 rsup 3 (%THETA_33-%THETA_32) # -%THETA_43 # 0 ## C lsup 5 rsup 1 %THETA_12 # 0 # C lsup 5 rsup 3 (%THETA_34-%THETA_32) # 0 # -%THETA_54} right ] underbrace {%OMEGA_%xi} left lbrace matrix{%xi_1 ## %xi_2 ## %xi_3 ## %xi_4 ## %xi_5} right rbrace underbrace {%xi}
left lbrace {matrix{v_1 ## v_2 ## v_3 ## v_4 ## v_5 }} right rbrace = {left [ {matrix{0 # 0 # 0 # 0 # 0 # U ## {tilde %beta_2} C lsup N rsup 1 # {tilde %rho}_21 C lsup N rsup 2 %GAMMA_1 # 0 # 0 # 0 # U ## {tilde %beta_3}C lsup N rsup 1 # 0 # {tilde %rho}_32 C lsup N rsup 3 %GAMMA_2 # 0 # 0 # U ## {tilde %beta}_4 C lsup N rsup 1 # 0 # {tilde %rho}_42 C lsup N rsup 3 %GAMMA_2 # {tilde %rho}_43 C lsup N rsup 4 %GAMMA_3 # 0 # U ## {tilde %beta}_5 C lsup N rsup 1 # 0 # {tilde %rho}_52 C lsup N rsup 3 %GAMMA_2 # 0 # {tilde %rho}_54 C lsup N rsup 5 %GAMMA_4 # U}}right ]} underbrace {V_u} {left lbrace {matrix{%omega_1 ## %sigma_1 ## %sigma_2 ## %sigma_3 ## %sigma_4 ## v_1}} right rbrace} underbrace {u}+ ~ newline {left [ {matrix{ 0 # 0 # 0 # 0 # 0 ## C lsup N rsup 1 %PSI_11 + {tilde{%rho}}_21 C lsup N rsup 1 %THETA_11 # -C lsup N rsup 2 %PSI_21 -{tilde %rho}_21 C lsup N rsup 2 %THETA_21 # 0 # 0 # 0 ## C lsup N rsup 1 %PSI_12 + {tilde{%rho}}_32 C lsup N rsup 1 %THETA_12 # 0 # -C lsup N rsup 3 %PSI_32 -{tilde %rho}_32 C lsup N rsup 3 %THETA_32 # 0 # 0 ## C lsup N rsup 1 %PSI_12 + {tilde{%rho}}_42 C lsup N rsup 1 %THETA_12 # 0 # C lsup N rsup 3 (%PSI_33 - %PSI_32) + {tilde{%rho}}_43 C lsup N rsup 3 %THETA_33 - {tilde{%rho}}_42 C lsup N rsup 3 %THETA_32 # -C lsup N rsup 4 %PSI_43 - {tilde %rho}_43 C lsup N rsup 4 %THETA_43 # 0 ## C lsup N rsup 1 %PSI_12 + {tilde{%rho}}_52 C lsup N rsup 1 %THETA_12 # 0 # C lsup N rsup 3 (%PSI_34 - %PSI_32) + {tilde{%rho}}_54 C lsup N rsup 3 %THETA_34 - {tilde{%rho}}_52 C lsup N rsup 3 %THETA_32 # 0# -C lsup N rsup 5 %PSI_54 - {tilde %rho}_54 C lsup N rsup 5 %THETA_54 }}right ]} underbrace {V_%xi} {left lbrace {matrix{%xi_1 ## %xi_2 ## %xi_3 ## %xi_4 ## %xi_5}} right rbrace} underbrace {%xi}

---
Observations
"Similar patterns arise in "~ %OMEGA_%xi, V_%xi " as arose in rigid-body "~ %OMEGA_u, V_u . newline newline "These patterns are a product of the recursive nature of the tree." newline newline "Non-zero entries trace the path from a body back to the root." newline newline "If body origins are at joints, then " newline %rho_21 = %rho_32 = %rho_43 = %rho_54 = 0 newline %PSI_21 , %PSI_32 , %PSI_43 , %PSI_54 "=" 0 newline %THETA_21 , %THETA_32 , %THETA_43 , %THETA_54 "=" 0

---
Conclusion
- Equations of motion have been derived for a system of flexible bodies connected by (spherical or gimballed) joints in a tree topology
- This formulation supports both free-free modes and cantilever modes

---
Appendix: Stress-Strain Relation
"Assuming a bulk material with a modulus of elasticity," E", and Poisson's ratio, " %nu "," newline "stress ("%sigma") and strain ("%epsilon") are related by" newline %sigma = S %epsilon newline "where" newline S = E over {1-%nu-2%nu^2}left [ matrix{1-%nu # %nu # %nu ## %nu # 1-%nu # %nu ## %nu # %nu # 1-%nu}right ] newline newline "Steel, as an example, has " E = 200 "GPa" newline "For many materials, "%nu = 0.2-0.3