Modeling Multi-Body Spacecraft Using Momentum State Dynamics
(MSD)
Eric Stoneking
October 2010

---
Objectives
- To formulate momentum state dynamics for Freespace, adding these capabilities
  - Tree topology
  - Flexible modes
  - 2-DOF and 3-DOF gimbal joints
  - Slider joints
  - Lockable joints
- By request, we seek to preserve the decoupling between the differential equations of motion

---
F = dot{p}" The rest is just accounting."

---
Rigid Bodies

---
Linear and Angular Momentum
"Linear Momentum: " P lsup N ^{B"*"} = m v lsup N ^{B"*"} = m v lsup N ^R + %omega lsup N ^B times c
c = m r lsup R ^{B"*"}
J " is moment of inertia of B about R"
R is fixed in B
(R may be joint or cm)
G undergoes arbitrary motion in N
B"*"
r lsup R ^{B"*"}
R
r lsup G ^R
"Angular Momentum of B about R:" H lsup R ^B = J %omega lsup N ^B - v lsup N ^R times c
r lsup N ^G
"Angular Momentum of B about G:" H lsup G ^B = H lsup R ^B + r lsup G ^R times P lsup N ^{B"*"}
N
G

---
MSD Equations of Motion
alignl dot{P} lsup N ^{B"*"} equiv {{d{P} lsup N ^{B"*"}} over dt} lsup N = F newline dot{H} lsup G ^{B} equiv {{d{H} lsup G ^B} over dt} lsup B = T_G - v lsup N ^G times P lsup N ^{B"*"} - %omega lsup N ^B times H lsup G ^B
"Since " dot{H} " and " dot{P} " appear alone on the lefthand side, the EOM may be integrated without" newline "solving a system of equations for them." newline newline "However, since " H " and " P " depend explicitly on " %omega " and " v ", a system of equations must still" newline "be solved at each evaluation of the EOM."

---
Example Problem
B_4
G_3
B_3
B_1
G_2
G_4
G_0
G_1
B_5
r lsup N ^{G_0}
B_2
N

---
Composite Momenta
"Let " P_k " be the linear momentum of the assembly of bodies outboard of the joint" G_k newline left lbrace P_k right rbrace = left lbrace {matrix{P_0 ## P_1 ## P_2 ## P_3 ## P_4} } right rbrace = left lbrace {matrix{P lsup {N} ^{B_1"*"} + P lsup {N} ^{B_2"*"} + P lsup {N} ^{B_3"*"} + P lsup {N} ^{B_4"*"} + P lsup {N} ^{B_5"*"} ## P lsup {N} ^{B_2"*"} ##P lsup {N} ^{B_3"*"} + P lsup {N} ^{B_4"*"} + P lsup {N} ^{B_5"*"}## P lsup {N} ^{B_4"*"} ## P lsup {N} ^{B_5"*"}}} right rbrace newline "Let " H_k " be the angular momentum of all bodies outboard of joint "G_k", about " G_k"." newline left lbrace H_k right rbrace = left lbrace {matrix{H_0 ## H_1 ## H_2 ## H_3 ## H_4} } right rbrace = left lbrace {matrix{H lsup {G_0} ^{B_1} + H lsup {G_0} ^{B_2} + H lsup {G_0} ^{B_3} + H lsup {G_0} ^{B_4} + H lsup {G_0} ^{B_5} ## H lsup {G_1} ^{B_2} ##H lsup {G_2} ^{B_3} + H lsup {G_2} ^{B_4} + H lsup {G_2} ^{B_5}## H lsup {G_3} ^{B_4} ## H lsup {G_4} ^{B_5}}} right rbrace newline newline [lbrace H_k rbrace, P_0] " are the momentum states chosen by Hughes in his text, and used in Freespace."

---
Handling Non-spherical Joints
"When all joints are spherical, the momentum states "[lbrace H_k rbrace, P_0]" form" newline "a minimum-dimension set of dynamical variables." newline newline "When some joints are 1-DOF or 2-DOF gimbals, it is advisable to" newline "reduce the order of the dynamical state accordingly." newline newline "Queen, London, and Gonzalez handled 1-DOF gimbals with" newline "scalar momentum states, which are the projection of " H_k " along" newline "the hinge axis." newline newline "We extend this technique to 2-DOF and 3-DOF gimbals using" newline "the idea of joint partials, as introduced in our development" newline "of multibody dynamics using Kane's method."

---
Joint Partials
Consider two bodies connected by a gimballed joint. The relative angular velocity
of the outer body, B, with respect to the inner body, A, may be written as a function
of the gimbal angles, , and the gimbal rates, . For example, a Body-3, 2-1-3
Euler rotation through gives:
%theta
%sigma equiv {dot %theta}
(%theta_1, %theta_2, %theta_3)
%omega lsup A rsup B = {left [matrix{c_2 s_3 # c_3 # 0 ## c_2 c_3 # -s_3 # 0 ## -s_2 # 0 # 1} right ]} underbrace {%GAMMA} {left lbrace {matrix{%sigma_1 ## %sigma_2 ## %sigma_3}} right rbrace } underbrace {%sigma}
"where "s_2 = sin(%theta_2), c_2 = cos(%theta_2), " etc, and the components of "%omega " are expressed in the" newline "frame of the outer body, B." newline newline "The matrix " %GAMMA " is called the matrix of joint partials. Each Euler sequence, including" newline "one- and two-DOF gimbals, has its own "%GAMMA". The dimensions of "%GAMMA" are 3 x NDOF." newline newline "For a spherical joint, "%sigma=%omega", and "%GAMMA = U", the identity matrix."

---
Joint Partials and Momentum States
"Noting that the columns of "~%GAMMA" are the components of the gimbal axes expressed in" newline "the joint's outer body frame, we define the scalar momentum states " newline h_{kj} equiv H_k cdot %GAMMA_{kj}, newline "or the 1-, 2-, or 3-DOF" newline h_k = %GAMMA^T_k H_k newline newline "The minimum-dimension angular momentum state vector then becomes:" newline left lbrace h_k right rbrace = left lbrace {matrix{h_0 ## h_1 ## h_2 ## h_3 ## h_4} } right rbrace = left lbrace {matrix{H lsup {G_0} ^{B_1} + H lsup {G_0} ^{B_2} + H lsup {G_0} ^{B_3} + H lsup {G_0} ^{B_4} + H lsup {G_0} ^{B_5} ## %GAMMA_1^T left (H lsup {G_1} ^{B_2} right ) ##%GAMMA_2^T left (H lsup {G_2} ^{B_3} + H lsup {G_2} ^{B_4} + H lsup {G_2} ^{B_5} right )## %GAMMA_3^T left (H lsup {G_3} ^{B_4} right ) ## %GAMMA_4^T left (H lsup {G_4} ^{B_5} right )}} right rbrace

---
Construction Preliminaries
"Using joint partials, we can systematically construct" newline "expressions for " [ lbrace H_k rbrace, P_0] " as functions of the minimum-" newline "dimension state vector, "u equiv [%sigma_k , v_0]. newline newline "To begin, let's define some terms:" newline %omega_i equiv %omega lsup N ^{B_i}newline v_k equiv v lsup N ^{G_k} newline alignl C lsup i ^j "is the direction cosine matrix between "B_i" and "B_j", " newline "so the components of a vector may be transformed thus:" v lsup i = C lsup i ^j v lsup j newline newline alignl %rho_ik " is the vector from "R_i" to "G_k". It is expressed in "N . newline
"The cross-product matrix is denoted by: "{tilde x} = left [ {matrix{0 # -x_3 # x_2 ## x_3 # 0 # -x_1 ## -x_2 # x_1 # 0}} right ],~~~~ x times y = {tilde x} y

---
Assembly Notation
"As we assemble the system, we adopt a not-uncommon notation to " newline "distinguish system-level properties from body-level properties." newline "In cases where a common symbol is used for both, the system-level" newline "vectors are enclosed in braces, "lbrace ` cdot ` rbrace", and system-level matrices are" newline "enclosed in brackets, "[ ` cdot ` ]" to reduce confusion."newline newline "For example, we use "J" to denote the inertia tensor of a generic " newline "single body. "J_i" denotes the inertia tensor of the "i"th body, and "[J]" denotes a" newline "system matrix formed by assembling the single-body inertia tensors:" newline [J] equiv "diag"[matrix{J_1 # J_2 # J_3 # dotslow} ]

---
Linear and Angular Velocities
left lbrace {matrix{%omega_1 ## %omega_2 ## %omega_3 ## %omega_4 ## %omega_5 }} right rbrace = {left [ {matrix{U # 0 # 0 # 0 # 0 # 0 ## C lsup 2 rsup 1 # %GAMMA_1 # 0 # 0 # 0 # 0 ## C lsup 3 rsup 1 # 0 # %GAMMA_2 # 0 # 0 # 0 ## C lsup 4 rsup 1 # 0 # C lsup 4 rsup 3 %GAMMA_2 # %GAMMA_3 # 0 # 0 ## C lsup 5 rsup 1 # 0 # C lsup 5 rsup 3 %GAMMA_2 # 0 # %GAMMA_4 # 0}}right ]} underbrace {%OMEGA} {left lbrace {matrix{%sigma_0 ## %sigma_1 ## %sigma_2 ## %sigma_3 ## %sigma_4 ## v_0}} right rbrace} underbrace {u}
left lbrace {matrix{v_0 ## v_1 ## v_2 ## v_3 ## v_4 }} right rbrace = {left [ {matrix{0 # 0 # 0 # 0 # 0 # U ## {tilde %rho}_20 C lsup N rsup 1 # {tilde %rho}_21 C lsup N rsup 2 %GAMMA_1 # 0 # 0 # 0 # U ## {tilde %rho}_30 C lsup N rsup 1 # 0 # {tilde %rho}_32 C lsup N rsup 3 %GAMMA_2 # 0 # 0 # U ## {tilde %rho}_40 C lsup N rsup 1 # 0 # {tilde %rho}_42 C lsup N rsup 3 %GAMMA_2 # {tilde %rho}_43 C lsup N rsup 4 %GAMMA_3 # 0 # U ## {tilde %rho}_50 C lsup N rsup 1 # 0 # {tilde %rho}_52 C lsup N rsup 3 %GAMMA_2 # 0 # {tilde %rho}_54 C lsup N rsup 5 %GAMMA_4 # U}}right ]} underbrace {V} {left lbrace {matrix{%sigma_0 ## %sigma_1 ## %sigma_2 ## %sigma_3 ## %sigma_4 ## v_0}} right rbrace} underbrace {u}

---
Body Momenta
"Using:" newline alignl P lsup N ^{B"*"} = m v lsup N ^R - c times %omega lsup N ^B, newline alignl H lsup R ^B = J %omega lsup N ^B + c times v lsup N ^R, newline newline "Let " newline alignl [m] equiv "diag"left [ matrix { m_1 U # m_2 U # m_3 U # m_4 U # m_5 U} right ] newline alignl [J] equiv "diag"left [ matrix { J_1 # J_2 # J_3 # J_4 # J_5} right ] newline alignl [tilde{c}] equiv "diag" left [ matrix { C lsup N ^1{tilde{c}}_1 # C lsup N ^2 {tilde{c}}_2 # C lsup N ^3 {tilde{c}}_3 # C lsup N ^4 {tilde{c}}_4 # C lsup N ^5 {tilde{c}}_5} right ] newline newline "yielding" newline alignl left lbrace P lsup N ^{B"*"} right rbrace = left [ [m]V - [tilde{c}] %OMEGA right ] u newline alignl left lbrace H lsup R ^B right rbrace = left [ [J] %OMEGA - [{tilde{c}}]^T V right ] u

---
Composite Momenta
"Using" newline H lsup G ^B = H lsup R ^B + r lsup G ^R times P lsup N ^{B"*"} newline "Let" newline S equiv left [ matrix {U # C lsup 1 ^2 # C lsup 1 ^3 # C lsup 1 ^4 # C lsup 1 ^5 ## ~ # U # ~ # ~ # ~## ~ # ~ # U # C lsup 3 ^4 # C lsup 3 ^5 ## ~ # ~ # ~ # U # ~ ## ~ # ~ # ~ # ~ # U} right ], ~~~~ R equiv left [ matrix {0 # C lsup 1 ^N {tilde{%rho}}_20 # C lsup 1 ^N {tilde{%rho}}_30 # C lsup 1 ^N {tilde{%rho}}_40 # C lsup 1 ^N {tilde{%rho}}_50 ## ~ # 0 # ~ # ~ # ~## ~ # ~ # 0 # C lsup 3 ^N {tilde{%rho}}_42 # C lsup 3 ^N {tilde{%rho}}_52 ## ~ # ~ # ~ # 0 # ~ ## ~ # ~ # ~ # ~ # 0} right ]newline newline "yielding" newline left lbrace H_k right rbrace = S left lbrace H lsup R ^B right rbrace - R left lbrace P lsup N ^{B"*"} right rbrace newline "or" newline left lbrace H_k right rbrace = left [ (S[J] + R [tilde{c}]) %OMEGA - (S [{tilde{c}}]^T + R [m]) V right ] u newline left lbrace h_k right rbrace = [%GAMMA_k]^T lbrace H_k rbrace = [%GAMMA_k]^T left [ (S[J] + R [tilde{c}]) %OMEGA - (S [{tilde{c}}]^T + R [m]) V right ] u newline "Similarly," newline %SIGMA equiv left [ matrix {U # U # U # U # U ## ~ # U # ~ # ~ # ~## ~ # ~ # U # U # U ## ~ # ~ # ~ # U # ~ ## ~ # ~ # ~ # ~ # U} right ] " gives " lbrace P_k rbrace = %SIGMA left [ [m]V-[tilde{c}] %OMEGA right ] u

---
Partial Momenta
"Define" newline alignl A = (S[J] + R [tilde{c}]) %OMEGA - (S [{tilde{c}}]^T + R [m]) V newline alignl %LAMBDA = left [ matrix{U # U # U # U # U} right ] left [ [m]V-[tilde{c}] %OMEGA right ] newline newline "so" newline alignl lbrace H_k rbrace = A u, ~~~~lbrace h_k rbrace = [%GAMMA_k]^T A u newline alignl P_0 = %LAMBDA u newline newline "In perfect analogy to "%OMEGA" and "V", "A" and "%LAMBDA" are, respectively," newline "the partial angular momenta and partial linear momenta" newline "relating "lbrace H_k rbrace" and "P_0" to the dynamic states, "u.

---
MSD Equations of Motion
"Integrate:" newline left lbrace stack{{dot{P}}_0 # lbrace {dot{h}}_k rbrace} right rbrace = left lbrace stack{F_0 # [%GAMMA_k]^T left lbrace T_k - v_k times P_k - Sum from i {%omega_i times H lsup {G_k} ^{B_i} }right rbrace} right rbrace newline "(where "F_0" is the total resultant force on the spacecraft," newline "applied at the center of mass, and "T_k" is the resultant torque " newline "about "G_k" of all forces and moments acting on bodies outboard of "G_k")" newline newline "Solve for "u":" newline left lbrace stack{P_0 # lbrace h_k rbrace} right rbrace = left [ matrix { %LAMBDA ## [%GAMMA_k]^T A} right ] u newline newline "Construct "lbrace %omega_i rbrace , lbrace %v_k rbrace ":" newline lbrace %omega_i rbrace = %OMEGA u newline lbrace v_k rbrace = V u newline "Repeat"

---
Locking a Single DOF
"To lock the jth DOF of joint "G_k", simply set "newline "the corresponding element of "u" to zero, and eliminate " newline "the corresponding "{dot{h}}_kj" from the EOM to be integrated."

---
Flexible Bodies

---
Linear and Angular Momentum
"Linear Momentum: " P lsup N ^{B"*"} = int from B {v lsup N ^{k} dm}
"Angular Momentum of B about R:"newline H lsup R ^B = int from B {left (r lsup R ^k times v lsup N ^k right ) dm}
dm
r_k
R
r lsup G ^R
r lsup N ^G
"Angular Momentum of B about G:" H lsup G ^B = H lsup R ^B + r lsup G ^R times P lsup N ^{B"*"}
N
G

---
Linear and Angular Momentum
"Linear Momentum: " newline matrix{P lsup N ^{B"*"} # "=" # alignl int from B {v lsup N ^{k} dm} ## " " # "=" #m v lsup N ^R + %omega lsup N ^B times (c+P_%PSI %eta) + P_%PSI %xi}
"Angular Momentum of B about R:"newline matrix{H lsup R ^B # "=" # alignl int from B {left (r lsup R ^k times v lsup N ^k right ) dm} ##" " # "=" # alignl int from B {(r_k+%PSI_k %eta) times left [v lsup N ^R + %omega lsup N ^B times (r_k + %PSI_k %eta) + %PSI_k %xi right ] dm} ##" " # "=" # alignl J %omega lsup N ^B - v lsup N ^R times (c+P_%PSI %eta) + (H_%PSI + Q_%PSI %eta) %xi - %omega lsup N ^B cdot (R_%PSI + R_%PSI^T) %eta }

---
Linear and Angular Velocities
left lbrace {matrix{%omega_1 ## %omega_2 ## %omega_3 ## %omega_4 ## %omega_5 }} right rbrace = {left [ {matrix{U # 0 # 0 # 0 # 0 # 0 ## C lsup 2 rsup 1 # %GAMMA_1 # 0 # 0 # 0 # 0 ## C lsup 3 rsup 1 # 0 # %GAMMA_2 # 0 # 0 # 0 ## C lsup 4 rsup 1 # 0 # C lsup 4 rsup 3 %GAMMA_2 # %GAMMA_3 # 0 # 0 ## C lsup 5 rsup 1 # 0 # C lsup 5 rsup 3 %GAMMA_2 # 0 # %GAMMA_4 # 0}}right ]} underbrace {%OMEGA_u} {left lbrace {matrix{%sigma_0 ## %sigma_1 ## %sigma_2 ## %sigma_3 ## %sigma_4 ## v_0}} right rbrace} underbrace {u}+ left [ matrix{0 # 0 # 0 # 0 # 0 ## C lsup 2 rsup 1 %THETA_11 # -%THETA_21 # 0 # 0 # 0 ##C lsup 3 rsup 1 %THETA_12 # 0 # -%THETA_32 # 0 # 0 ## C lsup 4 rsup 1 %THETA_12 # 0 # C lsup 4 rsup 3 (%THETA_33-%THETA_32) # -%THETA_43 # 0 ## C lsup 5 rsup 1 %THETA_12 # 0 # C lsup 5 rsup 3 (%THETA_34-%THETA_32) # 0 # -%THETA_54} right ] underbrace {%OMEGA_%xi} left lbrace matrix{%xi_1 ## %xi_2 ## %xi_3 ## %xi_4 ## %xi_5} right rbrace underbrace {%xi}
left lbrace {matrix{v_0 ## v_1 ## v_2 ## v_3 ## v_4 }} right rbrace = {left [ {matrix{0 # 0 # 0 # 0 # 0 # U ## {tilde %rho}_20 C lsup N rsup 1 # {tilde %rho}_21 C lsup N rsup 2 %GAMMA_1 # 0 # 0 # 0 # U ## {tilde %rho}_30 C lsup N rsup 1 # 0 # {tilde %rho}_32 C lsup N rsup 3 %GAMMA_2 # 0 # 0 # U ## {tilde %rho}_40 C lsup N rsup 1 # 0 # {tilde %rho}_42 C lsup N rsup 3 %GAMMA_2 # {tilde %rho}_43 C lsup N rsup 4 %GAMMA_3 # 0 # U ## {tilde %rho}_50 C lsup N rsup 1 # 0 # {tilde %rho}_52 C lsup N rsup 3 %GAMMA_2 # 0 # {tilde %rho}_54 C lsup N rsup 5 %GAMMA_4 # U}}right ]} underbrace {V_u} {left lbrace {matrix{%sigma_0 ## %sigma_1 ## %sigma_2 ## %sigma_3 ## %sigma_4 ## v_0}} right rbrace} underbrace {u}+ ~ newline {left [ {matrix{ 0 # 0 # 0 # 0 # 0 ## C lsup N rsup 1 %PSI_11 + {tilde{%rho}}_21 C lsup N rsup 1 %THETA_11 # -C lsup N rsup 2 %PSI_21 -{tilde %rho}_21 C lsup N rsup 2 %THETA_21 # 0 # 0 # 0 ## C lsup N rsup 1 %PSI_12 + {tilde{%rho}}_32 C lsup N rsup 1 %THETA_12 # 0 # -C lsup N rsup 3 %PSI_32 -{tilde %rho}_32 C lsup N rsup 3 %THETA_32 # 0 # 0 ## C lsup N rsup 1 %PSI_12 + {tilde{%rho}}_42 C lsup N rsup 1 %THETA_12 # 0 # C lsup N rsup 3 (%PSI_33 - %PSI_32) + {tilde{%rho}}_43 C lsup N rsup 3 %THETA_33 - {tilde{%rho}}_42 C lsup N rsup 3 %THETA_32 # -C lsup N rsup 4 %PSI_43 - {tilde %rho}_43 C lsup N rsup 4 %THETA_43 # 0 ## C lsup N rsup 1 %PSI_12 + {tilde{%rho}}_52 C lsup N rsup 1 %THETA_12 # 0 # C lsup N rsup 3 (%PSI_34 - %PSI_32) + {tilde{%rho}}_54 C lsup N rsup 3 %THETA_34 - {tilde{%rho}}_52 C lsup N rsup 3 %THETA_32 # 0# -C lsup N rsup 5 %PSI_54 - {tilde %rho}_54 C lsup N rsup 5 %THETA_54 }}right ]} underbrace {V_%xi} {left lbrace {matrix{%xi_1 ## %xi_2 ## %xi_3 ## %xi_4 ## %xi_5}} right rbrace} underbrace {%xi}

---
Effect of Flexibility on Rotation at Joints
"At joint "G_k", the relative attitude of the outer body, "B_o", with respect to the inner body, "B_i"," newline "must account for the rotation due to the flexibility of both bodies at the joint, as well as" newline "the \"rigid-body\" rotation due to the gimballed or spherical joint." newline newline "Introducing the intermediate frames "G_o" and "G_i" affixed, respectively, to the interfaces " newline "between the \"rigid\" joint and the outer and inner bodies,"
C lsup o ^i = {C lsup {Bo} ^{Go}} underbrace {C(%THETA_ko %eta_o)} {C lsup {Go} ^{Gi}} underbrace {C(%theta)} {C lsup {Gi} ^{Bi}} underbrace {C(%THETA_ki %eta_i)}
B_o
B_i
G_o
G_i

---
"Effect of Flexibility on " {tilde{%rho}}_ik
"Recall that "{tilde{%rho}}_ik" denotes the vector from the reference point "R_i" (fixed in the "i"th body, "B_i")" newline "to the "k"th joint, "G_k"." newline "We keep the same notation, but keep in mind that this vector now includes deflections " newline "due to flexibility ("%PSI %eta") as appropriate over the traversal from "R_i" to "G_k .

---
Body Momenta
"Using:" newline alignl P lsup N ^{B"*"} = m v lsup N ^R - (c+P_%PSI %eta) times %omega lsup N ^B + P_%PSI %xi, newline alignl H lsup R ^B = J %omega lsup N ^B - v lsup N ^R times (c+P_%PSI %eta) + (H_%PSI + Q_%PSI %eta) %xi - %omega lsup N ^B cdot (R_%PSI + R_%PSI^T) %eta , newline newline "Let " newline alignl {underline{J}}_i equiv (J-%eta^T(R_%PSI+R_%PSI^T))_i newline alignl [m] equiv "diag"left [ matrix { m_1 U # m_2 U # m_3 U # m_4 U # m_5 U} right ] newline alignl [underline{J}] equiv "diag"left [ matrix { {underline{J}}_1 # {underline{J}}_2 # {underline{J}}_3 # {underline{J}}_4 # {underline{J}}_5} right ] newline alignl [underline{tilde{c}}] equiv "diag" left [ matrix { C lsup N ^1(c+%P_%PSI %eta)^{`times`}_1 # C lsup N ^2 (c+%P_%PSI %eta)^{`times`}_2 # C lsup N ^3 (c+%P_%PSI %eta)^{`times`}_3 # C lsup N ^4 (c+%P_%PSI %eta)^{`times`}_4 # C lsup N ^5 (c+%P_%PSI %eta)^{`times`}_5} right ] newline alignl [P_%PSI] equiv "diag" left [ matrix {C lsup N ^1 P_{%PSI 1} # C lsup N ^2 P_{%PSI 2} # C lsup N ^3 P_{%PSI 3} # C lsup N ^4 P_{%PSI 4} # C lsup N ^5 P_{%PSI 5} } right ] newline alignl [{underline{H}}_%PSI] equiv "diag" left [ matrix{(H_%PSI + Q_%PSI %eta)_1 # (H_%PSI + Q_%PSI %eta)_2 # (H_%PSI + Q_%PSI %eta)_3 # (H_%PSI + Q_%PSI %eta)_4 # (H_%PSI + Q_%PSI %eta)_5} right ] newline newline "yielding" newline alignl lbrace P lsup N ^{B"*"} rbrace = left [ [m]V_u - [underline{tilde{c}}] %OMEGA_u right ] u + left [ [m] V_%xi - [underline{tilde{c}}] %OMEGA_%xi + [{P}_%PSI] right ] %xi newline alignl lbrace H lsup R ^B rbrace = left [ [underline{J}] %OMEGA_u - [underline{tilde{c}}]^T V_u right ] u+left [ [underline{J}] %OMEGA_%xi - [underline{tilde{c}}]^T V_%xi + [{underline{H}}_%PSI] right ] %xi

---
Composite Momenta
"Using" newline H lsup G ^B = H lsup R ^B + r lsup G ^R times P lsup N ^{B"*"} newline "Let" newline S equiv left [ matrix {U # C lsup 1 ^2 # C lsup 1 ^3 # C lsup 1 ^4 # C lsup 1 ^5 ## ~ # U # ~ # ~ # ~## ~ # ~ # U # C lsup 3 ^4 # C lsup 3 ^5 ## ~ # ~ # ~ # U # ~ ## ~ # ~ # ~ # ~ # U} right ], ~~~~ R equiv left [ matrix {0 # C lsup 1 ^N {tilde{%rho}}_20 # C lsup 1 ^N {tilde{%rho}}_30 # C lsup 1 ^N {tilde{%rho}}_40 # C lsup 1 ^N {tilde{%rho}}_50 ## ~ # 0 # ~ # ~ # ~## ~ # ~ # 0 # C lsup 3 ^N {tilde{%rho}}_42 # C lsup 3 ^N {tilde{%rho}}_52 ## ~ # ~ # ~ # 0 # ~ ## ~ # ~ # ~ # ~ # 0} right ]newline newline "yielding" newline lbrace H_k rbrace = S lbrace H lsup R ^B rbrace - R lbrace P lsup N ^{B"*"} rbrace newline "or" newline lbrace H_k rbrace = left [ (S [underline{J}] + R [underline{tilde{c}}]) %OMEGA_u - (S [underline{tilde{c}}]^T+ R [m]) V_u right ] u+left [ (S [underline{J}] + R [underline{tilde{c}}]) %OMEGA_%xi - (S [underline{tilde{c}}]^T + R[m]) V_%xi + S [{underline{H}}_%PSI] - R [P_%PSI] right ] %xi newline lbrace h_k rbrace = [%GAMMA_k]^T lbrace H_k rbrace newline "Similarly," newline %SIGMA equiv left [ matrix {U # U # U # U # U ## ~ # U # ~ # ~ # ~## ~ # ~ # U # U # U ## ~ # ~ # ~ # U # ~ ## ~ # ~ # ~ # ~ # U} right ] " gives " lbrace P_k rbrace = %SIGMA left lbrace left [ [m]V_u - [underline{tilde{c}}] %OMEGA_u right ] u + left [ [m] V_%xi - [underline{tilde{c}}] %OMEGA_%xi + [P_%PSI] right ] %xi right rbrace

---
Partial Momenta
"Define" newline alignl A_%PSI = left [ matrix {(S [underline{J}] + R [underline{tilde{c}}]) %OMEGA_u - (S [underline{tilde{c}}]^T+ R [m]) V_u # (S [underline{J}] + R [underline{tilde{c}}]) %OMEGA_%xi - (S [underline{tilde{c}}]^T + R[m]) V_%xi + S [{underline{H}}_%PSI] - R [P_%PSI] } right ] newline alignl %LAMBDA_%PSI = left [ matrix{U # U # U # U # U} right ] left [ matrix {[m]V_u - [underline{tilde{c}}] %OMEGA_u # [m] V_%xi - [underline{tilde{c}}] %OMEGA_%xi + [P_%PSI]} right ] newline newline "so" newline alignl lbrace H_k rbrace = A_%PSI left lbrace stack{u # %xi} right rbrace, ~~~~lbrace h_k rbrace = [%GAMMA_k]^T A_%PSI left lbrace stack{u # %xi} right rbrace newline alignl P_0 = %LAMBDA_%PSI left lbrace stack{u # %xi} right rbrace

---
Flexible Body Momenta
"The momentum states discussed so far are extensions of the rigid-body momentum " newline "states. We still need some equations of motion for the flexible modes of each body." newline "Ken London suggests we use the momentum states:" newline newline %PI equiv int_B {%PSI_k^T v lsup N ^k dm} newline "with the equations of motion:" newline dot{%PI} = int_B %PSI_k^T df newline "Expressing "v lsup N ^k" as:" newline v lsup N ^k = v lsup N ^R + %omega lsup N ^B times (r lsup R ^k + %PSI_k %eta) + %PSI_k %xi newline newline "and referring to modal integrals defined in Kane_NBody_Flex slides, we immediately obtain" newline newline %PI = P_%PSI ^T v lsup N ^R + (H_%PSI + Q_%PSI %eta)^T %omega lsup N ^B + M_%PSI %xi newline "or" newline lbrace %PI rbrace = left [ matrix{[{underline{H}}_%PSI]^T %OMEGA_u + [P_%PSI]^T V_u # [{underline{H}}_%PSI]^T %OMEGA_%xi + [P_%PSI]^T V_%xi + [M_%PSI] } right ] left lbrace stack{u # %xi} right rbrace newline "For compactness, we introduce "%PHI_%PSI , newline lbrace %PI rbrace = %PHI_%PSI left lbrace stack{u # %xi} right rbrace

---
MSD Equations of Motion
"Integrate:" newline left lbrace stack{{dot{P}}_0 # lbrace {dot{h}}_k rbrace # lbrace {dot{%PI}}_i rbrace } right rbrace = left lbrace stack{F_0 # [%GAMMA_k]^T left lbrace T_k - v_k times P_k - Sum from i {%omega_i times H lsup {G_k} ^{B_i} }right rbrace # left lbrace int_{B_i} %PSI^T df right rbrace} right rbrace newline "(where "F_0" is the total resultant force on the spacecraft, applied at the center of mass, and" newline alignl T_k" is the resultant torque about "G_k" of all forces and moments acting on bodies outboard of "G_k")." newline "As discussed in the Kane_NBody_Flex slides, "int_{B_i} %PSI^T df" comprises spring and damping" newline "forces, "-C_%PSI %xi - K_%PSI %eta", as well as any external forces or moments that have zero resultants on" newline "the body, but non-zero projections into the modal space."newline ""newline "Solve for "u, %xi":" ~~~ left lbrace stack{P_0 # lbrace h_k rbrace # lbrace %PI rbrace} right rbrace = left [ matrix { %LAMBDA_%PSI ## [%GAMMA_k]^T A_%PSI ## %PHI_%PSI} right ] left lbrace stack{u # %xi} right rbrace newline newline "Construct "lbrace %omega_i rbrace, lbrace %v_k rbrace":"~~~ stack{lbrace %omega_i rbrace = %OMEGA_u u + %OMEGA_%xi %xi # lbrace v_k rbrace = V_u u + V_%xi %xi} newline "Repeat"